## Slide 1: Hardware

## Slide 2
Boolean Logic

## Slide 3
Logic Model
Background
  Boolean algebra introduced by Gorge Boole. Mathematical logic and symbolic logic. Completeness of Nand and Nor. Digital logic gates. Claude Shannon’s circuit design theory.
Goal
  Understand the significance of Nand’s and Nor’s completeness. Learn about the logic operations in Boolean algebra and the functions of logic gates. The introduction of category theory in system design. Prepare for the implementation of combinational logic circuit.
Input
  Content: Nand gate.
  Studying Material:Nand2Tetris course of chapter one. Boolean algebra.Claude Shannon’s circuit theory.
  Tools:HDL and hardware simulator.
Process
  Learn about the Boolean algebra and with the understanding of the completeness of Nand operation as well as circuit design theory, use the given Nand gate to implement other basic logic gates in HDL. Test the gates in simulator.
Output
  Logic gates built in HDL.
  Test output.
  The demonstration of the completeness of Nand.
Effect
  Any basic gate’s can be built by only Nand, and these gates’ can perform any operations in Boolean algebra.
  The logical connection between the bottom design and the overall system.

## Slide 4
Contents
Project
  Logic gates: And, And16, DMux, DMux4Way, DMux8Way, Mux, Mux4Way16, Mux8Way16, Mux16, Not, Not16, Or, Or8Way, Or16, Xor.
Questions discussion:
  The completeness of Nand or Nor.
  The category theory.

## Slide 5
Connection
Boolean algebra and circuit design theory lay the fundamental of the computer system.
It is the bottom part in the category theory, and provide different gates as interface for later use.

## Slide 6
ALU

## Slide 7
Logic Model
Background
  We have known the completness of nand, and we have built some basicial combinational gates. So how to build a computer with these gates?
Goal
  Build the computing unit of computer architecture.
Input
  Content: ADD, REV, ALU.
  Studying Material: Nand2T course, the element of computing system.
  Tools: HDL and hardware simulator.
Process
  Add two numbers , half adder to full adder
  Consider about minus.
  And combine things together to build an ALU.
Output
  ALU, to build which we take several steps.
Effect
  Understanding the structure of ALU which does all the computing operations
  Get a clear vision of what to do next looking at ALU.

## Slide 8
Contents
Project
  ADD:
    Xor here, And for carrier
    Twice for a full adder
    16bit
  Rev for subtraction
    As the max of the data is for sure, we can use rev to do that.
  ALU:
    Deal with Input and Output
    Deal with operation
Questions discussion:
  University and waste

## Slide 9
Connection
ALU can do almost all the computing operations, as we can see later in as machine language.
So what else do we need?
  Where to get Input? Where to store output? (memory)
  What operation to do? Which operation to choice? (machine language, decode ,PC)

## Slide 10
Sequential logic

## Slide 11
Logic Model
Background
  We have discussed about combinational logic, which provide necessary abilities needed to build memory.
  We have built ALU, in which input and output is not defined.
Goal
  By combine combinational logic with DFF, we are going to build register and memory, using which we are closed to building whole the computer architecture.
Input
  Content: DFF, register, memory.
  Studying Material: Nand2T course, the element of computing system.
  Tools: HDL and hardware simulator.
Process
  Learn the property of DFF
  Build one-bit chips: register, PC
  Build a RAM4k
Output
  Build chips about memory needed in computer.
  Pass the test
Effect
  Understanding how computer stores data.
  Understanding Location, read ,write which are used in later chapters.

## Slide 12
Project
  Time: DFF:
  Option choice:
  Location choice:
Questions discussion:
  Why time?
  Comparison:
    With human mind, hard disk.
    Difference between register and RAM.
Contents

## Slide 13
Connection
Chapter1 (base)
CPU and assembly language
  Register and Memory
VM memory mapping
  Stack, heap, virtual register
Array and Object in high-level language

## Slide 14
Computer Architecture

## Slide 15
Logic Model
Background
  The chips built in the previous projects. The von Neumann architecture and relevant instructions.
Goal
  Learn about the von Neumann architecture. Use the chips built previously to make a general Hack computer. Understand the working of hardware. Prepare for the Hack assembler’s implementation.
Input
  Content: PC, RAM4K, RAM16K, ALU, Screen, Keyboard and all the more chips built before.
  Studying Material: Nand2T course, the element of computing system.
  Tools: HDL and hardware simulator.
Process
  Learn the property of DFF
  Build one-bit chips: register, PC
  Build a RAM4k
Output
  Memory.hdl
  CPU.hdl
  Computer.hdl
  Test programs’ working.
Effect
  The Hack computer built in HDL can run any Hack machine language programs on it successfully.
  The programs’ working supports the feasibility of von Neumann architecture and the completeness of Turing machine.

## Slide 16
Project: Hack computer
Question discussion: what are the other architectures? What are the differences among them?
Harvard, pipelining…
Contents

## Slide 17
Connection
Provide the hardware platform for the software part.
The instance of a hack computer shows the system of von Neumann architecture, and indicates the other architectures.

## Slide 18
Low-level Language

## Slide 19
Logic Model
Background
  The general-purpose Hack computer we built earlier, and the interface designed as the ALU's input.
Goal
  Consider again about the ALU and its input,which define a set of instructions and a machine language.Design an assembly language corresponding to this set and implement the compiler,making our first step towards software layer.
Input
  Content: Whole Hack Computer and the ALU I/O specification.Test assembly language scripts
  Studying Material: Nand2T course, the element of computing system.
  Tools: HDL and computer simulator.
Process
  Review the input bit set of ALU in Hack implementation
  Design Hack assembly language with one-to-one mapping with the bitstream.
  Build an assembler
Output
  Hack assembler
  Test programs’ working.
Effect
  The Hack Computer can take input as assembly language and act accordingly.
  The design of assembly language makes it easier to program on Hack platform.
  Design the first pseudo-software layer above the hardware implementation

## Slide 20
Project: Assembler
Question discussion: Why is the ALU designed to take bitset as it is designed previously? Is there any other ways to rebuild the ALU?Can assembly language represent any machine language?
Bootstrapping,a first and basic glance of Compiler and Interpreter…
Contents

## Slide 21
Connection
Provide the hardware platformta user-friendly interface to program on it .
Act as the base abstraction to be used for high-level language implementation
The Hack assembly language demonstrate a simplified way to build command sets on certain platform.It makes it easier to build platform-unrelated layer above it,which will be further discussed later in software part

## Slide 22
Hardware Part
BASE: Boolean Logic
MEM
PC..
compute
Store Data
Instructions decode
Flow control
C: COMP
A
C:Dest;comp
C: jump
Machine Language
ALU
Nand
DFF
[Chapter2]
[Chapter3]
[Chapter4]
[Chapter5]
[Chapter1]
Assembly language Abstraction