## Slide 1: Week 5
Joining the pieces

## Slide 2: Recap
What we’ve built so far
ALU
RAM chips
Elementary logic chips (And, Mux16, etc)
We know machine language inside and out

## Slide 3: How do we execute ANY command?
Theory
Universal Turing Machine
Practice
Von Neumann Architecture

## Slide 4: Universal Turing Machine

## Slide 5: Von Neumann Architecture

## Slide 7: Von Neumann vs Harvard Architecture
Von Neumann
  Same memory holds data & instructions
  Single set of address/data buses between CPU and memory
Harvard
  Separate memories for data (RAM) and instructions (ROM)
  Two sets of address/data buses between CPU and memory
  Allows for two simultaneous data fetches

## Slide 8: Von Neumann vs Harvard Architecture
Harvard
  Greater memory bandwidth
  More predictable bandwidth

## Slide 9: RISC vs CISC
Reduced Instruction Set Computer (RISC)
  Compact, uniform instructions facilitate pipelining
  More lines of code = large memory footprint
  Allow effective compiler optimization
Complex Instruction Set Computer (CISC)
  Many addressing modes and long instructions
  High code density
  Often require manual optimization of assembly code for embedded systems

## Slide 10: Adding two numbers
The RISC approach
@0
D=M
@1
D=D+M
@2
M=D
The CISC approach
ADD @0, @1

## Slide 11: RISC vs CISC
RISC
Emphasis on software
Single-clock
Large code size,
Lower cycles per second
Independently LOAD and STORE
CISC
Emphasis on hardware
Multi-clock instructions
Small code size
More cycles per second
LOAD and STORE incorporated in different functions

## Slide 12: The advantage of RISC
Similar execution time
Separate LOAD and STORE functions actually lessen load
More room for general purpose registers
Uniform execution time allows for pipelining

## Slide 13: Example
RISC | ARM7 | ARM9
CISC | Pentium | SHARC DSP
 | Von Neumann | Harvard

## Slide 14: General computer vs dedicated computer
Which of the below is a general computer?
  Apple iPhone
  HDTV
  PC
  Industrial control unit